## Slide 1
8th EuReComp Webinar „Repurposing End-of-Life Wind Turbine Blades – Case Study: Composite Floaters for Floating PV Systems”
Dr. Andreia Araújo, Prof. Robert Böhm
30.10.2025

## Slide 2: Agenda
8th EuReComp Webinar – A. Araújo, R. Böhm
    Introduction
    Why is repurposing of EoL wind turbine blades important?
    R6-strategy and case study selection
    Small scale demonstrator
    Large scale demonstrator
    Summary & Outlook

## Slide 3: Introduction
8th EuReComp Webinar – A. Araújo, R. Böhm
This subproject of EuReComp was jointly realized by INEGI (Porto, Portugal) and HTWK Leipzig (Germany).
Photo INEGI people (Andreia)

## Slide 4: Problem: Circularity of composites
8th EuReComp Webinar – A. Araújo, R. Böhm
Reference: WindEurope
European Green Deal requires net zero emission until 2045.
Concepts of circularity have to be established for composites.

## Slide 5: Problem: Circularity of composites
8th EuReComp Webinar – A. Araújo, R. Böhm
End-of-Life (EoL) wind turbine blade (WTB) composite waste represents a rapidly growing global waste stream: quantity of EoL WTB’s in Europe alone: 100,000 tons annually until 2034 [Albers et al.]
What to do with the “waste”?  Need to recycle!
 Composites are expensive high-performance materials!

## Slide 6: Circularity of composites: existing solutions
8th EuReComp Webinar – A. Araújo, R. Böhm
Recycling by pyrolysis
Reusing (chopped) fibres for other applications
Pyrolysis is not a relevant WTB recycling solution in terms of sustainability and economic meaningfulness: too expensive for GFRP and not sustainable for CFRP
Recovered fibres (mostly chopped) are used as a filler for concrete, for BMC’s or for low value applications. Problem: Composite structural integrity is destroyed
[Thornmann]
[Larsen]

## Slide 7: Circular economy: circularity strategies
8th EuReComp Webinar – A. Araújo, R. Böhm
Circularity strategies according to [Potting et al. 2017] within the production chain, in order of priority:
  Definition of “Repurpose”: Use of a product in a new product with a different function. These new applications are usually of lower value than the original.

## Slide 8: R6-strategy
8th EuReComp Webinar – A. Araújo, R. Böhm
Scheme of interaction within the R6-strategy: “Reuse by …” [Johst et al. 1]
Hierarchy / Priorization (Tier 1-3)

## Slide 9: Repurposing of WTBs: materials
8th EuReComp Webinar – A. Araújo, R. Böhm
0,2 m
Sandwich design
Composite design (shells)
Aluminium
Adhesive
UD GFRP
BD GFRP
Foam / Balsa wood
Gelcoat
[Kucher et al. 2023]

## Slide 10: Repurposing of WTBs: multi-scale problem
8th EuReComp Webinar – A. Araújo, R. Böhm
Glass fibre
Polymer matrix
(epoxy resin)
Micro scale
Meso scale
Sub-structural scale
Structural scale

## Slide 11: Repurposing: definitions and classifications
8th EuReComp Webinar – A. Araújo, R. Böhm
Scenario 1
Repurposing is not a single manufacturing step but a complex treatment strategy with several process steps:
  Different actors and technologies are involved
  Dependencies between the different processes and stakeholders
The constellation of actors, technologies and institutions that are connected is called ecosystem.
Classification of repurpose scenarios (depending on WTB damage state, disassembly location and geometry)
EoL WTB structure as a whole
High to moderate loading conditions
Proof-of-design problem
Scenario 2
EoL WTB structure as a whole
Low loading conditions
No proof-of-design problem
Scenario 3
EoL WTB structure partially cut
High to moderate loading conditions
Proof-of-design problem
Scenario 4
EoL WTB structure partially cut
Low loading conditions
No proof-of-design problem

## Slide 12: Scenario 3 demo: floating PV systems
8th EuReComp Webinar – A. Araújo, R. Böhm
Source: https://www.energynet.de/2021/06/10/schwimmende-photovoltaikanlagen/
Further expansion of renewable energies
Advantages: saving of usable space on land (Asia); higher efficiency (no cooling); no solid structures needed (foundation); less water evaporation
Companies: Intersolar, RWE, BayWa, Ocean Sun, Ciel & Terre, HelioRec, Yellow Tropus, LE GmbH etc.
Floating body
PV-Module
Problems with current Floating PV’s: high costs for floating bodies; required high robustness especially on sea

## Slide 13: Scenario 3 demo: floating PV systems
8th EuReComp Webinar – A. Araújo, R. Böhm
Solar panel
E40 EoL segment
Closing ends
Support structure of solar panel
FRP pultruded profiles or grating
2x 5m WTB sections
Replace standard aluminium supports with FRP beams from spar cap
Idea: Using EoL WTB parts as a replacement of the floating body [Moutinho et al.]
Lightweight, robust, high-performance properties, designed towards fatigue resistance
Low cost for EoL materials
Small scale demo – 1 PV panel
Large scale demo – 4 PV panels
Upscaling

## Slide 14: Small scale demo: concept
8th EuReComp Webinar – A. Araújo, R. Böhm
Concept small-scale pontoon
E40 EoL WTB segment
E40 blade
Solar panel
E40 EoL segment
Closing ends
Support structure of solar panel
Preliminary design concept for small-scale demo
Concept of the small-scale demo:
Realizing floating capability (closing of ends, sealing)
Connection technology (support structure of PV module/s)
Load application via the spar caps

## Slide 15: Small scale demo: concept
8th EuReComp Webinar – A. Araújo, R. Böhm
Center of gravity determination

## Slide 16: Small scale demo: concept
8th EuReComp Webinar – A. Araújo, R. Böhm

## Slide 17: Small scale demo manufacturing: (1) WTB preparation
8th EuReComp Webinar – A. Araújo, R. Böhm
Cutting surface
Manual grinding
Polished surface

## Slide 18: Small scale demo manufacturing: (2) Load introduction
8th EuReComp Webinar – A. Araújo, R. Böhm
Mounting 4 profile holders for frame construction
Sealing the holes with waterproof glue
Drilling 4 holes in the spar caps and 2 in the trailing edge
“Cavity dowel”

## Slide 19: Small scale demo manufacturing: (3) Closing ends
8th EuReComp Webinar – A. Araújo, R. Böhm
Waterproof glue on grinded surface and fastening of a PMMA closer
Drying of the glue

## Slide 20: Small scale demo manufacturing: (4) Experiments
8th EuReComp Webinar – A. Araújo, R. Böhm
Specimen preparation from the spar caps for material characterization

## Slide 21: Small scale demo manufacturing: (5) Support structure
8th EuReComp Webinar – A. Araújo, R. Böhm
Assembly of the support structure

## Slide 22: Small scale demo manufacturing: (6) Solar module
8th EuReComp Webinar – A. Araújo, R. Böhm
Assembly of the solar module

## Slide 23: Small scale demo manufacturing: (7) Floating test
8th EuReComp Webinar – A. Araújo, R. Böhm

## Slide 24: Andreia
8th EuReComp Webinar – A. Araújo, R. Böhm

## Slide 25: Andreia
8th EuReComp Webinar – A. Araújo, R. Böhm

## Slide 26: Andreia
8th EuReComp Webinar – A. Araújo, R. Böhm

## Slide 27: Andreia
8th EuReComp Webinar – A. Araújo, R. Böhm

## Slide 28: Andreia
8th EuReComp Webinar – A. Araújo, R. Böhm

## Slide 29: Andreia
8th EuReComp Webinar – A. Araújo, R. Böhm

## Slide 30: Andreia
8th EuReComp Webinar – A. Araújo, R. Böhm

## Slide 31: Andreia
8th EuReComp Webinar – A. Araújo, R. Böhm

## Slide 32: Andreia
8th EuReComp Webinar – A. Araújo, R. Böhm

## Slide 33: Life-Cycle Assessment (LCA)
8th EuReComp Webinar – A. Araújo, R. Böhm
Does a EoL WTB repurpose have positive environmental effects at all?

## Slide 34: Life-Cycle Assessment (LCA)
8th EuReComp Webinar – A. Araújo, R. Böhm
Six environmental impact categories were considered in [Johst et al. 2]: Global warming potential (GWP), acidification (AP), ozone depletion (ODP), land use, eutrophication (EP), and photochemical ozone formation
Within our analysis, we examined a relatively light WTB (component mass approx. 1000 kg). The results are not directly transferable to larger WTB’s, as the emissions of the transport processes are highly mass-dependent. For our repurpose approach, the transport from wind parks to the repurpose locations has the biggest impact.

## Slide 35: Lessons learnt
8th EuReComp Webinar – A. Araújo, R. Böhm
Andreia: if you like, put some stuff here in the style of  too much manual work,  automation required,  follow-up project with floating PV guys would be nice etc.

## Slide 36: Summary and outlook
8th EuReComp Webinar – A. Araújo, R. Böhm
Repurposing of large EoL composite structures like wind turbine blades is scientifically meaningful and socially necessary.
  First practical solutions have been developed in EuReComp.
  Societal transformation (circular economy) asks for quick large-volume answers. Many questions in this context remain important:
    The design guideline problem: material properties and data
    Life-Cycle Assessment
    Material quantity problem
    National and international regulations

## Slide 37: Literature
8th EuReComp Webinar – A. Araújo, R. Böhm
[Albers et al.] H. Albers, S. Greiner, H. Seifert, and U. Kuehne, “Recycling of wind turbine rotor blades. Fact or fiction?: Recycling von Rotorblaettern aus Windenergieanlagen. Fakt oder Fiktion?,” (in English; German), DEWI-Magazin, 2009. [Online]. Available: https://​www.osti.gov​/​etdeweb/​biblio/​21214142
[Potting et al.] J. Potting, M. Hekkert, E. Worrell, and A. Hanemaaijer, “Circular Economy: Measuring innovation in the product chain,” Accessed: Jan. 25 2023. [Online]. Available: https://​www.pbl.nl​/​sites/​default/​files/​downloads/​pbl-​2016-​circular-​economy-​measuring-​innovation-​in-​product-​chains-​2544.pdf
[Johst et al. 1] P. Johst, M. Kucher, P. Schulz, A. Knorr, R. Kupfer, and R. Böhm, “Identification of circular eco-subsystems for end-of-life aviation composite components based on a systematized R6-strategy,” vol. 2526, no. 1, p. 12055, 2023, doi: 10.1088/1742-6596/2526/1/012055.
[Larsen] K. Larsen, “Recycling wind turbine blades,” Renewable Energy Focus, vol. 9, no. 7, pp. 70–73, 2009, doi: 10.1016/S1755-0084(09)70045-6.
[Schmid et al.] M. Schmid, N. Ramon, A. Dierckx, and T. Wegman, WindEurope-Accelerating-wind-turbine-blade-circularity. [Online]. Available: https://​windeurope.org​/​wp-​content/​uploads/​files/​about-​wind/​reports/​WindEurope-​Accelerating-​wind-​turbine-​blade-​circularity.pdf (accessed: Jan. 23 2023).
[Kucher et al.] M. Kucher, P. Johst, M. Lizaranzu, F. Lahuerta, and R. Böhm, “A Micromechanical Modeling Approach for the Estimation of the Weathering-Induced Degradation of Wind Turbine Blades,” Mater Circ Econ, 2023, doi: 10.1007/s42824-023-00088-4.
[Ullah et al.] Z. Ullah, S.A. Grammatikos, M.C. Evernden, C.J. Pearce, C. J. (2017). Multi-scale computational homogenisation to predict the long-term durability of composite structures. Computers & Structures, 181, 21-31
[Johst et al. 2] P. Johst, M. Kucher, M. Bühl, P. Schulz, R. Kupfer, L. Schilling, R.M. Santos, C. Carneiro, P. Voigt, N. Modler, and R. Böhm, “Identification of circular ecosystems for the repurpose of decommissioned large-scale composite structures.” Materials Circular Economy (2023), 5 (13), https://doi.org/10.1007/s42824-023-00085-7
[Johst et al. 3] JOHST, P.; LI, S., KIM, E.; BAE, S.; BÖHM, R.; NA, W.: Structural integrity assessment of reused wind turbine blade composite components with acou-stic emission testing and Ib-value analysis. Composites Part B: Engineering 301 (2025) 112490, https://doi.org/10.1016/j.compositesb.2025.112490
[Moutinho et al.] MOUTINHO, M.; ROCHA, R.; ATTELN, D.; JOHST, P.; BÖHM, R.; CHATZIPANAGIOTOU, K.-R.; STAMKOPOULOU, E.; KOUMOULOS, E.P.; ARAÚJO, A.: Repurposing EoL WTB components into a large-scale PV-floating demonstrator. Sustainability (2025), 17, 8717. https://doi.org/10.3390/su17198717

## Slide 38
Prof. Robert Böhm
robert.boehm@htwk-Leipzig.de
HTWK Leipzig (Germany)
Dr. Andreia Araújo
aaraujo@inegi.up.pt
INEGI Porto (Portugal)